/*****************************************************

This program was produced by the

CodeWizardAVR V2.04.4a Advanced

Automatic Program Generator

© Copyright 1998-2009 Pavel Haiduc, HP InfoTech s.r.l.

http://www.hpinfotech.com

Project : SENSOR NIXIE CLOCK

Version : 321

Date    : 22.12.2010

Author  : coolish.ru

Company : NEC-HITACHI Corp.

Comments: MADE IN CHINA

Chip type               : ATmega32L

Program type            : Application

AVR Core Clock frequency: 7,372800 MHz

Memory model            : Small

External RAM size       : 0

Data Stack size         : 512

*****************************************************/

#include <mega32.h>

#include <stdlib.h>

#include <delay.h>

#include <sleep.h>

#include <ds1621_36.h>

// --------- Date processing

#define    EPOCH_YR        1970

#define    SECS_DAY        86400UL

#define    LEAPYEAR(year)    (!((year) % 4) && (((year) % 100) || !((year) % 400)))

#define    YEARSIZE(year)    (LEAPYEAR(year) ? 366 : 365)

long timeDAY(unsigned char tm_hour, unsigned char tm_minute, unsigned char tm_sec)

{

return tm_sec + 60L * (tm_minute + 60L * tm_hour);

}

unsigned char MONTHSIZE(unsigned char isleapyear, unsigned char month){

if(month==2){

return(28+isleapyear);

}

if (month>7){

month--;

}

if (month%2==0){

return(30);

}

return(31);

}

unsigned long int strtotime(unsigned int tm_year, unsigned char tm_mon, unsigned char tm_day, unsigned char tm_hour, unsigned char tm_minute, unsigned char tm_sec)

{

unsigned long int res = 0;

unsigned char leapyear;

tm_day--;

tm_mon--;

// day

leapyear = LEAPYEAR(tm_year);

while (tm_year > EPOCH_YR) {

tm_year--;

res += YEARSIZE(tm_year);

}

while (tm_mon > 0) {

res += MONTHSIZE(leapyear, tm_mon);

tm_mon--;

}

res += tm_day;

res *= SECS_DAY;

// seconds

res += (unsigned long int)tm_sec + 60 * ((unsigned long int)tm_minute + 60 * (unsigned long int)tm_hour);

return res;

}

void timetostr(unsigned long int time, unsigned int *tm_year, unsigned char *tm_mon, unsigned char *tm_day, unsigned char *tm_hour, unsigned char *tm_min, unsigned char *tm_sec, unsigned char *tm_wday)

{

unsigned long int dayclock;

unsigned int dayno;

unsigned char leapyear;

register unsigned int atm_year;

register unsigned char atm_mon;

atm_year = EPOCH_YR;

dayclock = time % SECS_DAY;

dayno = time / SECS_DAY;

if (tm_sec) *tm_sec = (unsigned char)(dayclock % 60UL);

if (tm_min) *tm_min = (unsigned char)((dayclock % 3600UL) / 60);

if (tm_hour) *tm_hour = (unsigned char)(dayclock / 3600UL);

if (tm_wday) *tm_wday = (dayno + 4) % 7;

while (dayno >= YEARSIZE(atm_year)) {

dayno -= YEARSIZE(atm_year);

atm_year++;

}

leapyear = LEAPYEAR(atm_year);

atm_mon = 1;

while (dayno >= MONTHSIZE(leapyear, atm_mon)) {

dayno -= MONTHSIZE(leapyear, atm_mon);

atm_mon++;

}

if (tm_year) *tm_year = atm_year;

if (tm_mon) *tm_mon = atm_mon;

if (tm_day) *tm_day = dayno + 1;

}

// --------- Date processing - END

// --------- Autosync

#define AUTOSYNCMAXSTAT     (24*60*60)

typedef struct {

unsigned char status;          // 0 - процесс не идёт, 1 - процесс идёт, 2 - идёт сохранение статистики

unsigned long int stat_msectotal;

unsigned long int stat_msec;

unsigned long int stat_pulsestotal;

unsigned long int correct_10msec;

long int correct_delta;

} AUTOSYNC;

AUTOSYNC autosync;

eeprom unsigned long int autosync_msectotal_eep @ 4;

eeprom unsigned long int autosync_pulsestotal_eep @ 8;

void load_autosync()

{

unsigned long int autosync_pulsestotal_temp;

unsigned long int autosync_msectotal_temp;

unsigned long int autosync_correct_10msec_temp;

long int autosync_correct_delta_temp;

// Загрузка значений автокалибровки

autosync_pulsestotal_temp = autosync_pulsestotal_eep;

autosync_msectotal_temp = autosync_msectotal_eep;

autosync_correct_10msec_temp = autosync_pulsestotal_temp * 100;

autosync_correct_delta_temp = 10 * autosync_correct_10msec_temp - autosync_msectotal_temp; // -499..499

while (autosync_correct_delta_temp > 499) {

autosync_correct_delta_temp >>= 1;

autosync_correct_10msec_temp >>= 1;

#asm("wdr");

}

while (autosync_correct_delta_temp < -499) {

autosync_correct_delta_temp >>= 1;

autosync_correct_delta_temp |= 0x80000000;

autosync_correct_10msec_temp >>= 1;

#asm("wdr");

}

// Если явные глюки - то лучше поставить калибровку по нулям

if (

autosync_pulsestotal_temp == 0xFFFFFFFF || autosync_msectotal_temp == 0xFFFFFFFF || autosync_correct_10msec_temp < 100 * 60 ||

(autosync_pulsestotal_temp + 10) < (autosync_msectotal_temp / 1000) ||

(autosync_pulsestotal_temp - 10) > (autosync_msectotal_temp / 1000)

) {

#asm("cli");

autosync.correct_delta = 0;

autosync.correct_10msec = 0xFFFFFFFF;

#asm("sei");

} else {

#asm("cli");

autosync.correct_delta = autosync_correct_delta_temp;

autosync.correct_10msec = autosync_correct_10msec_temp;

#asm("sei");

}

}

// Timer 0 output compare interrupt service routine. Autosync aysnchorous calibrating timer

interrupt [TIM0_COMP] void timer0_comp_isr(void)

{

if (autosync.status == 1) {

autosync.stat_msec += 10;

}

ir.loopcounter += 0x0048;

}

// --------- Autosync - END

// --------- Timekeeper

#define UTCOffset (3 * 60 * 60)             // +3 часа

#define DaylightOffset (60 * 60)            // +1 час

#define DaylightSaving 1                    // использовать переход лето-зима

#define MAXSYNC 3

#define MAXFAIL (60*9)

typedef struct {

long int msec;

unsigned long int unixtime;

unsigned char fl_timeupdate;

unsigned char fl_dosync;

unsigned char sync_counter;

unsigned int fail_counter;

long int msec_sync;

unsigned long int unixtime_sync;

unsigned char DDMMYYHHMMSSMMM_sync[16];

unsigned char time1PPS;

unsigned char time1Sync;

unsigned char timeStatus;               // 0 - запуск, 1 - время шло, 2 - время точно синхронизировано

unsigned char tm_sec_old;

} TIMEKEEPER;

TIMEKEEPER timekeeper = { 0, 0, 0, 0, 0, 0, 0, 0, {0}, 0, 0, 0, 0 };

// Timer1 output compare A interrupt service routine. Main timekeeper timer

interrupt [TIM1_COMPA] void timer1_compa_isr(void)

{

timekeeper.msec += 10;

if (timekeeper.timeStatus == 1) {  // автономный ход

static unsigned long int autosync_correct_thr = 0;

static long int msec_correct_delta = 0;

autosync_correct_thr++;

if (autosync_correct_thr >= autosync.correct_10msec) {

autosync_correct_thr = 0;

msec_correct_delta = autosync.correct_delta;

}

if (msec_correct_delta) {

long int tmp;

if ((tmp = timekeeper.msec + msec_correct_delta) > 0) {

timekeeper.msec = tmp;

msec_correct_delta = 0;

}

}

}

if (timekeeper.msec >= 1000) timekeeper.fl_timeupdate = 1;

if (buttons.button2_drb) buttons.button2_drb--;

if (buttons.button3_drb) buttons.button3_drb--;

if (buttons.button4_drb) buttons.button4_drb--;

if (buttons.button5_drb) buttons.button5_drb--;

if (sensors.movement_drb) sensors.movement_drb--;

}

// External Interrupt 2 service routine. 1PPS interrupt

interrupt [EXT_INT2] void ext_int2_isr(void)

{

int frac;

// Пустить таймер с нуля

TCNT1H = 0x00;

TCNT1L = 0x00;

// Округлить к ближайшей секунде

frac = timekeeper.msec % 1000;

if (frac < 500) {

timekeeper.msec -= frac;

timekeeper.msec_sync -= frac;

} else {

frac = 1000 - frac;

timekeeper.msec += frac;

timekeeper.msec_sync += frac;

timekeeper.fl_timeupdate = 1;

}

// У нас есть точная синхронизация 1PPS

timekeeper.time1PPS = 4;

timekeeper.time1Sync = 4;

// Авто калибровка

if (autosync.status == 0) {

autosync.stat_msectotal = 0;

autosync.stat_msec = 0;

autosync.stat_pulsestotal = 0;

TCNT0 = 0;

TIFR |= 0x02;   // OCF0

autosync.status = 1;

//TIMSK |= 0x02;

} else if (autosync.status == 1) {

if (autosync.stat_msec < 950 || autosync.stat_msec > 1050 || autosync.stat_pulsestotal > AUTOSYNCMAXSTAT) {  // Набор статистики не более суток

autosync.status = 2;

} else {

autosync.stat_pulsestotal++;

autosync.stat_msectotal += autosync.stat_msec;

autosync.stat_msec = 0;

}

}

}

// --------- Timekeeper - END

// --------- GPS Receiver

#define FRAMING_ERROR           (1<<FE)

#define PARITY_ERROR            (1<<UPE)

#define DATA_OVERRUN            (1<<DOR)

#define DATA_REGISTER_EMPTY     (1<<UDRE)

#define RX_COMPLETE             (1<<RXC)

// Set SIRF 4800

flash unsigned char SIRF_INIT0[33] = "\r\n\r\n\r\n$PSRF100,0,4800,8,1,0*0F\r\n";

flash unsigned char SIRF_INIT0_len = 32;

// Set NMEA 57600

flash unsigned char SIRF_INIT1[32] = { 0xA0, 0xA2, 0x00, 0x18, 0x81, 0x02, 0x01, 0x01, 0x01, 0x01, 0x05, 0x01, 0x05, 0x01, 0x01, 0x01, 0x01, 0x01, 0x00, 0x01, 0x00, 0x01, 0x00, 0x01, 0x00, 0x01, 0xE1, 0x00, 0x01, 0x7C, 0xB0, 0xB3 };

flash unsigned char SIRF_INIT1_len = 32;

// Set message rate, Reset RTC

flash unsigned char SIRF_INIT2[163] = "\r\n\r\n\r\n$PSRF101,0,0,0,0,0,0,12,4*10\r\n$PSRF103,0,0,0,1*24\r\n$PSRF103,1,0,0,1*25\r\n$PSRF103,2,0,0,1*26\r\n$PSRF103,3,0,0,1*27\r\n$PSRF103,4,0,1,1*21\r\n$PSRF103,5,0,0,1*21\r\n";

flash unsigned char SIRF_INIT2_len = 162;

const unsigned char RMC_tpl[8] = "$GPRMC,";

typedef struct {

unsigned char SIRF_STARTUP_pos;

unsigned char RMC[128];

unsigned char RMC_cs;

} RECEIVER;

RECEIVER receiver;

// USART Receiver interrupt service routine

interrupt [USART_RXC] void usart_rx_isr(void)

{

char status,data;

static unsigned char RMC_pos = 0;

static long int msec_sync_temp;

static unsigned long int unixtime_sync_temp;

status = UCSRA;

data = UDR;

if ((status & (FRAMING_ERROR | PARITY_ERROR | DATA_OVERRUN)) == 0)

{

// RMC load

if (RMC_pos == 0) {

receiver.RMC_cs = 0;

msec_sync_temp = timekeeper.msec;

unixtime_sync_temp = timekeeper.unixtime;

} else {

receiver.RMC_cs ^= data;

}

if (RMC_pos > 6) {

receiver.RMC[RMC_pos]=data; RMC_pos++;

if (RMC_pos == 120) RMC_pos = 0;

if (data == 13) {

if (receiver.RMC[RMC_pos-4]=='*') {

// Check CS

unsigned char cs_t, cs1, cs2;

cs1 = receiver.RMC[RMC_pos-3];

cs2 = receiver.RMC[RMC_pos-2];

receiver.RMC_cs ^= 13;

receiver.RMC_cs ^= '*';

receiver.RMC_cs ^= cs1;

receiver.RMC_cs ^= cs2;

if (cs1 <= '9') cs_t = (cs1 - '0'); else cs_t = (cs1 + 10 - 'A');

cs_t <<= 4;

if (cs2 <= '9') cs_t += (cs2 - '0'); else cs_t += (cs2 + 10 - 'A');

if (receiver.RMC_cs == cs_t && (!timekeeper.fl_dosync)) {

// if previous sync fully passed

// $GPRMC,051444.479,A,4712.9455,N,03937.5654,E,0.00,0.00,141108,,,A*68

unsigned char date_start;

unsigned char commas;

date_start = 15;

for (commas = 1; commas <= 8; date_start++) {

if (receiver.RMC[date_start] == ',') {

commas++;

}

if (date_start > RMC_pos) break;

}

// DDMMYY

timekeeper.DDMMYYHHMMSSMMM_sync[0] = receiver.RMC[date_start];

timekeeper.DDMMYYHHMMSSMMM_sync[1] = receiver.RMC[date_start+1];

timekeeper.DDMMYYHHMMSSMMM_sync[2] = receiver.RMC[date_start+2];

timekeeper.DDMMYYHHMMSSMMM_sync[3] = receiver.RMC[date_start+3];

timekeeper.DDMMYYHHMMSSMMM_sync[4] = receiver.RMC[date_start+4];

timekeeper.DDMMYYHHMMSSMMM_sync[5] = receiver.RMC[date_start+5];

// HHMMSS

timekeeper.DDMMYYHHMMSSMMM_sync[6] = receiver.RMC[7];

timekeeper.DDMMYYHHMMSSMMM_sync[7] = receiver.RMC[8];

timekeeper.DDMMYYHHMMSSMMM_sync[8] = receiver.RMC[9];

timekeeper.DDMMYYHHMMSSMMM_sync[9] = receiver.RMC[10];

timekeeper.DDMMYYHHMMSSMMM_sync[10] = receiver.RMC[11];

timekeeper.DDMMYYHHMMSSMMM_sync[11] = receiver.RMC[12];

// MMM

timekeeper.DDMMYYHHMMSSMMM_sync[12] = receiver.RMC[14];

timekeeper.DDMMYYHHMMSSMMM_sync[13] = receiver.RMC[15];

timekeeper.DDMMYYHHMMSSMMM_sync[14] = receiver.RMC[16];

timekeeper.msec_sync = msec_sync_temp;

timekeeper.unixtime_sync = unixtime_sync_temp;

timekeeper.fl_dosync = 1;

}

}

RMC_pos = 0;

}

} else {

receiver.RMC[RMC_pos] = data;

if (receiver.RMC[RMC_pos] == RMC_tpl[RMC_pos]) RMC_pos++; else RMC_pos = 0;

}

};

}

void usart_send(flash unsigned char *SIRF_INIT, unsigned char SIRF_INIT_len)

{

unsigned char SIRF_INIT_pos = 0;

while (SIRF_INIT_pos < SIRF_INIT_len) {

while (!(UCSRA & (unsigned char)(1 << UDRE))) {

#asm("wdr");

};

UDR = SIRF_INIT[SIRF_INIT_pos++];

}

}

// --------- GPS Receiver - END

// --------- Power management

#define PMAINPOWER   PINA.7

unsigned char fl_power = 0;

void clear_display()

{

hD1(0xFF, 0xFF);

hD2(0xFF, 0xFF);

hD3(0xFF, 0xFF);

hD4(0xFF, 0xFF);

hD5(0xFF, 0xFF);

hD6(0xFF, 0xFF);

hDiv1(0x00, 0xFF);

hDiv2(0x00, 0xFF);

}

void power_on()

{

clear_display();

// Set defaults

sensors.light = 0xFF;

sensors.temperature = 666;

sensors.movement_drb = 0xFF;

sensors.movement = 0;

output.brightness = 0xFF;

// Clear flags

#asm("cli");

timekeeper.fl_dosync = 0;

timekeeper.fl_timeupdate = 0;

#asm("sei");

timekeeper.sync_counter = MAXSYNC;

timekeeper.fail_counter = MAXFAIL;

// Set display to clock

output.display = 0;

output.depoisonState = 0;

menu.menuState = 0;

// Авто калибровка не идёт.

autosync.status = 0;

// ADC initialization

// ADC Clock frequency: 57,600 kHz

// ADC Voltage Reference: AVCC pin

// Only the 8 most significant bits of

// the AD conversion result are used

ADMUX = 0b01100000 | 0b00000011;	// ADC3

ADCSRA = 0b10000111; //0x87;

// External Interrupt(s) initialization

// INT0: On

// INT0 Mode: Falling Edge

// INT1: On

// INT1 Mode: Any change

// INT2: On

// INT2 Mode: Falling Edge

GIFR |= 0x60;

GICR |= 0x20;

// Display phase management

PORTB &= ~0b00001000;

// Timer/Counter 2 initialization

// Clock source: System Clock

// Clock value: 921,600 kHz

// Mode: Phase correct PWM top=FFh

// OC2 output: Non-Inverted PWM

PORTD &= ~0b10000000;

TCNT2 = 0x00;

OCR2 = 0x00;

TCCR2 = 0x62;

// 2 Wire Bus initialization

// Generate Acknowledge Pulse: Off

// 2 Wire Bus Slave Address: 0h

// General Call Recognition: Off

// Bit Rate: 250.000Khz

TWSR = 0x00;

TWBR = 0x00;

TWAR = 0x00;

TWCR = (1<<TWEN);

// DS1621 Thermometer/Thermostat initialization

// tlow: 50°C

// thigh: 55°C

// Tout polarity: 1

ds1621_init(0,50,55,1);

// SPI initialization

// Clear the SPI interrupt flag

#asm

in   r30,spsr

in   r30,spdr

#endasm

// Ports

//DDRB |= 0b10110000;

PORTA &= ~0b00000100;

//DDRA |= 0b00000100;

// SPI initialization

// SPI Type: Master

// SPI Clock Rate: 2*115,200 kHz

// SPI Clock Phase: Cycle Half

// SPI Clock Polarity: Low

// SPI Data Order: MSB First

SPCR = 0xD2;

SPSR = 0x01;

// Start shift update loop

hShift_pos = 0;

SPDR = 13;

// USART initialization

// Communication Parameters: 8 Data, 1 Stop, No Parity

// USART Receiver: On

// USART Transmitter: On

// USART Mode: Asynchronous

// USART Baud Rate: 4800

UCSRA = 0x00;

UCSRB = 0x18;

UCSRC = 0x86;

UBRRH = 0x00;

UBRRL = 0x5F;

receiver.SIRF_STARTUP_pos = 13;

fl_power = 1;

}

void main(void)

{

// --------- Init peripheral

// Watchdog Timer initialization

// Watchdog Timer Prescaler: OSC/2048k

WDTCR = 0x0F;

// Input/Output Ports initialization

PORTA = 0x00;

DDRA = 0x00;

PORTB = 0x00;

DDRB = 0x00;

PORTC = 0x00;

DDRC = 0x00;

PORTD = 0x00;

DDRD = 0x00;

// Timer/Counter 0 initialization

// Clock source: System Clock

// Clock value: 7,200 kHz

// Mode: CTC top=OCR0

// OC0 output: Disconnected

TCCR0 = 0x0D;

TCNT0 = 0x00;

OCR0 = 0x47;  // 0..71 (72 spots)

// Timer/Counter 1 initialization

// Clock source: System Clock

// Clock value: 7,200 kHz

// Mode: CTC top=OCR1A

// OC1A output: Discon.

// OC1B output: Discon.

// Noise Canceler: Off

// Input Capture on Falling Edge

// Timer1 Overflow Interrupt: Off

// Input Capture Interrupt: Off

// Compare A Match Interrupt: On

// Compare B Match Interrupt: Off

TCCR1A = 0x00;

TCCR1B = 0x0D;

TCNT1H = 0x00;

TCNT1L = 0x00;

ICR1H = 0x00;

ICR1L = 0x00;

OCR1AH = 0x00;

OCR1AL = 0x47;

OCR1BH = 0x00;

OCR1BL = 0x00;

// Timer/Counter 2 initialization

// Clock source: System Clock

// Clock value: Timer2 Stopped

// Mode: Normal top=FFh

// OC2 output: Disconnected

ASSR = 0x00;

OCR2 = 0x00;

TCCR2 = 0x00;

TCNT2 = 0x00;

// External Interrupt(s) initialization

// INT0: Off

// INT1: Off

// INT2: Off

MCUCR = 0x00;

MCUCSR = 0x00;

// Timer(s)/Counter(s) Interrupt(s) initialization

TIMSK = 0x10; // Main timekeeper

// Analog Comparator initialization

// Analog Comparator: Off

// Analog Comparator Input Capture by Timer/Counter 1: Off

ACSR = 0x80;

SFIOR = 0x00;

// --------- Init peripheral - END

// --------- Initial values

clear_display();

autosync.status = 0;

load_autosync();

TIMSK |= 0x02; // Async calibrate timer

// Кнопки не нажаты

PORTC |= 0b00111100;

// Movement sensor power control

PORTA &= ~0b0000001;

DDRA |= 0b0000001;

// Display phase management

PORTB &= ~0b00001000;

DDRB |= 0b00001000;

// Piezo

PORTD &= ~0b00110000;

PORTD |= ~0b00100000;

DDRD |= 0b00110000;

// Timer/Counter 2 PWM Output initialization

PORTD &= ~0b10000000;

DDRD |= 0b10000000;

// External Interrupt(s) initialization

// INT0: On

// INT0 Mode: Falling Edge

// INT1: On

// INT1 Mode: Any change

// INT2: On

// INT2 Mode: Falling Edge

GIFR |= 0xE0;

MCUCR = 0x06;

MCUCSR = 0x00;

GICR |= 0x80;

PORTD |= 0b00001100;

PORTB |= 0b00000100;

// SPI initialization Ports

PORTB &= ~0b10110000;

DDRB |= 0b10110000;

PORTA &= ~0b00000100;

DDRA |= 0b00000100;

// --------- Initial values - END

// --------- Main loop

#asm("sei");

while (1)

{

unsigned int tm_year, tm_msec;

unsigned long int tm_unixtime;

unsigned char tm_mon, tm_day, tm_wday, tm_hour, tm_min, tm_sec;

long int tm_delta;

// Sleep and watchdog mode

#asm("wdr");

if (!fl_power) {

sleep_enable();

idle();

sleep_disable();

}

// Check if sync is pending

if (timekeeper.fl_dosync) {

timekeeper.DDMMYYHHMMSSMMM_sync[15] = 0;

tm_msec = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[12]);

timekeeper.DDMMYYHHMMSSMMM_sync[12] = 0;

tm_sec = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[10]);

timekeeper.DDMMYYHHMMSSMMM_sync[10] = 0;

tm_min = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[8]);

timekeeper.DDMMYYHHMMSSMMM_sync[8] = 0;

tm_hour = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[6]);

timekeeper.DDMMYYHHMMSSMMM_sync[6] = 0;

tm_year = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[4]) + 2000;

timekeeper.DDMMYYHHMMSSMMM_sync[4] = 0;

tm_mon = atoi(&timekeeper.DDMMYYHHMMSSMMM_sync[2]);

timekeeper.DDMMYYHHMMSSMMM_sync[2] = 0;

tm_day = atoi(timekeeper.DDMMYYHHMMSSMMM_sync);

if (tm_year >= 2010) {

tm_unixtime = strtotime(tm_year, tm_mon, tm_day, tm_hour, tm_min, tm_sec);

tm_delta = 0;

if (timekeeper.time1PPS) {

// don't touch msec < 1000

timekeeper.msec_sync = 1000 * ((timekeeper.msec / 1000) - (timekeeper.msec_sync / 1000));

} else {

// full sync with msec

timekeeper.msec_sync = tm_msec - timekeeper.msec_sync;

}

// Check sync delta

tm_delta = timekeeper.msec_sync;

if (tm_unixtime >= timekeeper.unixtime_sync) {

if (tm_unixtime - timekeeper.unixtime_sync > 5) tm_delta = 666; else tm_delta += 1000 * (tm_unixtime - timekeeper.unixtime_sync);

} else {

if (timekeeper.unixtime_sync - tm_unixtime > 5) tm_delta = 666; else tm_delta -= 1000 * (timekeeper.unixtime_sync - tm_unixtime);

}

if ( (tm_delta < 100 && tm_delta > -100) || timekeeper.sync_counter == 0) {

// Была синхронизация

timekeeper.timeStatus = 2;

timekeeper.time1Sync = 4;

if (tm_delta >= 0 && tm_delta < 100) {

timekeeper.msec_sync = tm_delta;

} else {

if (tm_unixtime >= timekeeper.unixtime_sync) {

timekeeper.unixtime_sync = tm_unixtime - timekeeper.unixtime_sync;

timekeeper.unixtime += timekeeper.unixtime_sync;

} else {

timekeeper. unixtime_sync = timekeeper.unixtime_sync - tm_unixtime;

timekeeper.unixtime -= timekeeper.unixtime_sync;

}

}

#asm("cli");

timekeeper.msec += timekeeper.msec_sync;

#asm("sei");

timekeeper.sync_counter = MAXSYNC;

} else {

timekeeper.sync_counter--;

}

timekeeper.fail_counter = MAXFAIL;

} else {

if (timekeeper.fail_counter) {

timekeeper.fail_counter--;

} else {

timekeeper.fail_counter = MAXFAIL;

// reset sirf

usart_send(&SIRF_INIT2[0], SIRF_INIT2_len);

}

if (timekeeper.timeStatus == 2) timekeeper.timeStatus = 1;

}

#asm("cli");

timekeeper.fl_dosync = 0;

#asm("sei");

}

if (timekeeper.fl_timeupdate) {

// Firstly do msec counter process

unsigned int passed = timekeeper.msec / 1000;

unsigned int passedmsec = passed * 1000;

unsigned long int delta;

int timeDaylightSaving = 0;

// Disable interrupts & do shit with msec counter

#asm("cli");

timekeeper.fl_timeupdate = 0;

timekeeper.msec -= passedmsec;

timekeeper.msec_sync -= passedmsec;

#asm("sei");

// It may have passed some seconds

timekeeper.unixtime += passed;

// calculate offset

timetostr(timekeeper.unixtime, 0, &tm_mon, &tm_day, 0, 0, 0, &tm_wday);

delta = 0;

if (DaylightSaving) {

// Посчитаем, летнее ли время??

if (tm_mon>3 && tm_mon<10) {

// between Mart(3) && October(10) - SUMMER MODE

timeDaylightSaving = DaylightOffset;

} else if (tm_mon == 3) {

// greater than last Sunday?

if (tm_day >= (31 - (((31-tm_day) + tm_wday) % 7))) timeDaylightSaving = DaylightOffset;

} else if (tm_mon == 10) {

// lower than last Sunday?

if (tm_day < (31 - (((31-tm_day) + tm_wday) % 7))) timeDaylightSaving = DaylightOffset;

}

delta += timeDaylightSaving;

}

// Учтём смещение от UTC.

delta += UTCOffset;

// Calculate local time

timetostr(timekeeper.unixtime + delta, &tm_year, &tm_mon, &tm_day, &tm_hour, &tm_min, &tm_sec, 0);

// Second change handlers

if (tm_sec != timekeeper.tm_sec_old) {

if (settings.tickSetting == 1) {

if (sensors.light < 64) {

tick_start(1, tm_sec);

} else if (sensors.light > 192) {

tick_start(3, tm_sec);

} else {

tick_start(2, tm_sec);

}

} else if (settings.tickSetting == 3) {

tick_start(settings.tickVolume, tm_sec);

}

}

// Output to display

if (fl_power) {

if ( (timekeeper.unixtime > output.depoisonLast + DEPOISONINTERVAL || output.depoisonLast == 0) && output.depoisonState == 0 && alarms.alarmState == 0) {

movement_sensor_on();

output.depoisonState = DEPOISONCYCLES;

}

if (output.depoisonState) {

unsigned char x1 = output.depoisonState % 10;

unsigned char x2 = output.depoisonState & 0b00000111;

hD1(x1, 0xFF);

hD2(x1, 0xFF);

hD3(x1, 0xFF);

hD4(x1, 0xFF);

hD5(x1, 0xFF);

hD6(x1, 0xFF);

hDiv1(x2, 0xFF);

hDiv2(x2, 0xFF);

output.depoisonState--;

if (output.depoisonState == 0) {

movement_sensor_off();

output.depoisonLast = timekeeper.unixtime;

}

}

if (output.depoisonState == 0) {

if (output.display == 0) {

if (timekeeper.timeStatus == 0) {

hD1(0xFF, 0xFF);

hD2(0xFF, 0xFF);

hD3(0xFF, 0xFF);

hD4(0xFF, 0xFF);

hD5(0xFF, 0xFF);

hD6(0xFF, 0xFF);

} else {

hD1(tm_hour / 10, 0xFF);

hD2(tm_hour % 10, 0xFF);

// Minute

hD3(tm_min / 10, 0xFF);

hD4(tm_min % 10, 0xFF);

// Second

hD5(tm_sec / 10, 0xFF);

hD6(tm_sec % 10, 0xFF);

}

if (tm_sec != timekeeper.tm_sec_old) {

switch (timekeeper.timeStatus) {

case 0: case 1:

hDiv1(1, 0xFF);

hDiv2(1, 0xFF);

delay_ms(30);

#asm("wdr");

hDiv1(0, 0xFF);

hDiv2(0, 0xFF);

delay_ms(30);

#asm("wdr");

hDiv1(1, 0xFF);

hDiv2(1, 0xFF);

delay_ms(30);

#asm("wdr");

hDiv1(0, 0xFF);

hDiv2(0, 0xFF);

break;

case 2:

if (timekeeper.time1PPS) {

hDiv1(tm_sec & 1, 0xFF);

hDiv2(tm_sec & 1, 0xFF);

} else {

hDiv1(1, 0xFF);

hDiv2(1, 0xFF);

delay_ms(30);

#asm("wdr");

hDiv1(0, 0xFF);

hDiv2(0, 0xFF);

}

break;

}

}

} else if (output.display & 0b00000011) {

int xx = sensors.temperature;

if (xx >= 0) hDiv1(2, 0xFF); else hDiv1(4, 0xFF);

hDiv2(0, 0xFF);

hD1(0xFF, 0xFF);

hD2(0xFF, 0xFF);

hD3(xx / 100, 0xFF); xx = xx % 100;

hD4(xx / 10, 0xFF); xx = xx % 10;

hD5(xx, 0xFF);

hD6(0xFF, 0xFF);

output.display &= ~0b00000001;

}

}

}

// SIRF Startup queue?

if (fl_power && receiver.SIRF_STARTUP_pos && timekeeper.tm_sec_old != tm_sec)

{

receiver.SIRF_STARTUP_pos--;

if (receiver.SIRF_STARTUP_pos == 10) {//                delay_ms(2500>>2);

// switch to SIRF@4800

usart_send(&SIRF_INIT0[0], SIRF_INIT0_len);

}

if (receiver.SIRF_STARTUP_pos == 7) {//              delay_ms(2500>>2);

// Switch to NMEA@57600

usart_send(&SIRF_INIT1[0], SIRF_INIT1_len);

}

if (receiver.SIRF_STARTUP_pos == 5) {              //delay_ms(1000>>2);

// USART Baud Rate: 57600

UBRRH=0x00;

UBRRL=0x07;

}

if (receiver.SIRF_STARTUP_pos == 3) {       //delay_ms(1500>>2);

// Reset RTC, Set message rate NMEA@57600

usart_send(&SIRF_INIT2[0], SIRF_INIT2_len);

}

if (receiver.SIRF_STARTUP_pos == 1) {       //delay_ms(1500>>2);

UCSRB = 0x98;   // enable RX interrupt

}

}

if (timekeeper.tm_sec_old != tm_sec) sensors.temperature = ds1621_temperature_10(0);

// Second change handlers finished

timekeeper.tm_sec_old = tm_sec;

// Idle every second

if (timekeeper.time1PPS) timekeeper.time1PPS--;

if (timekeeper.time1Sync) timekeeper.time1Sync--;

// Вероятный переход в режим автономного хода

if (!timekeeper.time1Sync && timekeeper.timeStatus == 2) timekeeper.timeStatus = 1;

// Авто калибровка запись в eeprom

if (autosync.status == 2 || (autosync.status && !timekeeper.time1PPS)) {

#asm("cli");

autosync.status = 2;

#asm("sei");

//TIMSK &= ~0x02;

if (autosync_pulsestotal_eep == 0xFFFFFFFF || autosync_msectotal_eep == 0xFFFFFFFF || autosync.stat_pulsestotal > autosync_pulsestotal_eep || autosync.stat_pulsestotal >= AUTOSYNCMAXSTAT) {

autosync_msectotal_eep = autosync.stat_msectotal;

autosync_pulsestotal_eep = autosync.stat_pulsestotal;

}

#asm("cli");

autosync.status = 0;

#asm("sei");

// Загрузить новые калибровочные значения

load_autosync();

}

}

// Check if main power is went away

if (fl_power && (PMAINPOWER == 0)) { // Power off.

power_off();

}

// Check if main power is on

if (!fl_power && (PMAINPOWER == 1)) { // Power on.

power_on();

}

// --------- Main loop - END

}